## Slide 1
Instructor: Alexander Stoytchev
http://www.ece.iastate.edu/~alexs/classes/
CprE 281: Digital Logic

## Slide 2
Design Examples
CprE 281: Digital Logic
Iowa State University, Ames, IA
Copyright © Alexander Stoytchev

## Slide 3: Administrative Stuff
HW3 is due on Monday Sep 16 @ 10pm
Please write clearly on the first page the following three things:
  Your First and Last Name
  Your Student ID Number
  Your Lab Section Letter
Submit on Canvas as *one* PDF file.
Please orient your pages such that the text can be read without the need to rotate the page.

## Slide 4: Quick Review

## Slide 5: Axioms of Boolean Algebra
1a. 0  0 = 0
1b. 1 + 1 = 1
2a. 1  1 = 1
2b. 0 + 0 = 0
3a. 0  1 = 1  0 = 0
3b. 1 + 0 = 0 + 1 = 1
4a. If x=0, then
4b. If x=1, then
x = 1
x = 0

## Slide 6
x
1
x
2
x
1
x
2
+
AND gate
x
x
x
1
x
2
x
1
x
2
•
The Three Basic Logic Gates
[ Figure 2.8 from the textbook ]
OR gate
NOT gate

## Slide 7: Single-Variable Theorems
5a. x  0 = 0
5b. x + 1 = 1
6a. x  1 = x
6b. x + 0 = x
7a. x  x = x
7b. x + x = x
8a. x 
8b. x +
9.
x = 0
x = 1
x = x

## Slide 8: Two- and Three-Variable Properties
10a. x  y = y  x
10b. x + y = y + x
11a. x  (y  z) = (x  y)  z
11b. x + (y + z) = (x + y) + z
12a. x  (y + z) = xy + xz
12b. x + y  z = (x + y)(x + z)
13a. x + x  y = x
13b. x  (x + y) = x
Commutative
Associative
Distributive
Absorption

## Slide 9: Two- and Three-Variable Properties
14a. x  y + x 
14b. (x + y)(x +
15a. x  y = x + y
15b. x + y = x  y
16a. x + xy = x + y
16b. x(x + y) = xy
17a. xy + yz + xz = xy + xz
17b. (x+y)(y+z)(x+z)=(x+y)(x+z)
Combining
DeMorgan’s
theorem
Consensus
y = x
y) = x

## Slide 10: NAND Gate
x1 | x2 | f
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 11: NOR Gate
x1 | x2 | f
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 12: Why do we need two more gates?
They can be implemented with fewer transistors.
Each of the new gates can be used to implement
the three basic logic gates: NOT, AND, OR.

## Slide 13: Implications
Any Boolean function can be implemented
with only NAND gates!

## Slide 14: Implications
Any Boolean function can be implemented
with only NAND gates!
The same is also true for NOR gates!

## Slide 15: minterms (for two variables)

## Slide 16: The Four minterms
x | y | m0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | m1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | m2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | m3
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
m3(x, y)
m0(x, y)
m1(x, y)
m2(x, y)

## Slide 17: The Four minterms
x | y | m0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | m1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | m2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | m3
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
m3(x, y)
m0(x, y)
m1(x, y)
m2(x, y)

## Slide 18: The Four minterms
x | y |  | m0(x, y) | m1(x, y) | m2(x, y) | m3(x, y)
0 | 0 |  | 1 | 0 | 0 | 0
0 | 1 |  | 0 | 1 | 0 | 0
1 | 0 |  | 0 | 0 | 1 | 0
1 | 1 |  | 0 | 0 | 0 | 1

## Slide 19: The Four minterms
x | y |  | x y | x y | x y | x y
0 | 0 |  | 1 | 0 | 0 | 0
0 | 1 |  | 0 | 1 | 0 | 0
1 | 0 |  | 0 | 0 | 1 | 0
1 | 1 |  | 0 | 0 | 0 | 1

## Slide 20: Circuits for the four minterms
y
x
x
y
x
y
x
y
m3(x, y) = x y
m0(x, y) = x y
m1(x, y) = x y
m2(x, y) = x y

## Slide 21: Maxterms (for two variables)

## Slide 22: The Four Maxterms
x | y | M0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | y | M1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | M2
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | M3
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
M3(x, y)
M0(x, y)
M1(x, y)
M2(x, y)

## Slide 23: The Four Maxterms
x | y | M0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | y | M1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | M2
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | M3
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
M3(x, y)
M0(x, y)
M1(x, y)
M2(x, y)

## Slide 24: The Four Maxterms
x | y |  | M0(x, y) | M1(x, y) | M2(x, y) | M3(x, y)
0 | 0 |  | 0 | 1 | 1 | 1
0 | 1 |  | 1 | 0 | 1 | 1
1 | 0 |  | 1 | 1 | 0 | 1
1 | 1 |  | 1 | 1 | 1 | 0

## Slide 25: The Four Maxterms
x | y |  | x + y | x + y | x + y | x + y
0 | 0 |  | 0 | 1 | 1 | 1
0 | 1 |  | 1 | 0 | 1 | 1
1 | 0 |  | 1 | 1 | 0 | 1
1 | 1 |  | 1 | 1 | 1 | 0

## Slide 26: minterms and Maxterms (for two variables)

## Slide 27: minterms and Maxterms
x | y | m0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
x | y | m1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
x | y | m2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
x | y | m3
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
x | y | M0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
x | y | M1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 1
1 | 1 | 1
x | y | M2
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
x | y | M3
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 28: minterms and Maxterms
m3(x, y) = x y
m0(x, y) = x y
m1(x, y) = x y
m2(x, y) = x y
M0(x, y) = x + y
M3(x, y) = x + y
M1(x, y) = x + y
M2(x, y) = x + y

## Slide 29: minterms (for three variables)

## Slide 30: The Eight minterms
x | y | z | m0 | m1 | m2 | m3 | m4 | m5 | m6 | m7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 31: The Eight minterms
x | y | z | m0 | m1 | m2 | m3 | m4 | m5 | m6 | m7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 32: Expressions for the minterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z

## Slide 33: Expressions for the minterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The bars coincide
with the 0’s
in the binary expansion
of the minterm sub-index

## Slide 34: Maxterms (for three variables)

## Slide 35: The Eight Maxterms
x | y | z | M0 | M1 | M2 | M3 | M4 | M5 | M6 | M7
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0

## Slide 36: The Eight Maxterms
x | y | z | M0 | M1 | M2 | M3 | M4 | M5 | M6 | M7
0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0

## Slide 37: Expressions for the Maxterms
M0 = x + y + z
M1 = x + y + z
M2 = x + y + z
M3 = x + y + z
M4 = x + y + z
M5 = x + y + z
M6 = x + y + z
M7 = x + y + z

## Slide 38: Expressions for the Maxterms
M0 = x + y + z
M1 = x + y + z
M2 = x + y + z
M3 = x + y + z
M4 = x + y + z
M5 = x + y + z
M6 = x + y + z
M7 = x + y + z
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
The bars coincide
with the 1’s
in the binary expansion
of the maxterm sub-index

## Slide 39: minterms and Maxterms (for three variables)

## Slide 40: minterms and Maxterms
m0 = x y z
m1 = x y z
m2 = x y z
m3 = x y z
m4 = x y z
m5 = x y z
m6 = x y z
m7 = x y z
M0 = x + y + z
M1 = x + y + z
M2 = x + y + z
M3 = x + y + z
M4 = x + y + z
M5 = x + y + z
M6 = x + y + z
M7 = x + y + z

## Slide 41: Synthesis Example

## Slide 42: Truth table for a three-way light control
[ Figure 2.31 from the textbook ]

## Slide 43: Let’s Derive the SOP form

## Slide 44: minterms and Maxterms (with three variables)
[ Figure 2.22 from the textbook ]

## Slide 45: Let’s Derive the SOP form

## Slide 46: Let’s Derive the SOP form
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3

## Slide 47: Let’s Derive the SOP form
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3

## Slide 48: Let’s Derive the SOP form
x1 x2 x3
x1 x2 x3
x1 x2 x3
x1 x2 x3

## Slide 49: Sum-of-products realization
f
x1
x3
x2
[ Figure 2.32a from the textbook ]

## Slide 50: Let’s Derive the POS form
[ Figure 2.31 from the textbook ]

## Slide 51: Let’s Derive the POS form

## Slide 52: minterms and Maxterms (with three variables)
[ Figure 2.22 from the textbook ]

## Slide 53: Let’s Derive the POS form

## Slide 54: Let’s Derive the POS form
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )

## Slide 55: Let’s Derive the POS form
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )

## Slide 56: Let’s Derive the POS form
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )
( x1 + x2 + x3 )

## Slide 57: Product-of-sums realization
f
x3
x1
x2
[ Figure 2.32b from the textbook ]

## Slide 58: Function Synthesis

## Slide 59: Example 2.10
Implement the function f(x1, x2, x3) = Σ m(2, 3, 4, 6, 7)

## Slide 60: Minterms and Maxterms (with three variables)
[ Figure 2.22 from the textbook ]

## Slide 61: minterms and Maxterms (with three variables)

## Slide 62
The SOP expression is:
This could be simplified as follows:

## Slide 63: Recall Property 14a
14a. x  y + x 
14b. (x + y)(x +
Combining
y = x
y) = x

## Slide 64: SOP realization of the function
[ Figure 2.30a from the textbook ]
f
x2
x3
x1
The SOP expression is: f = x2 + x1x3

## Slide 65: Example 2.12
Implement the function f(x1, x2, x3) = Π M(0, 1, 5),
which is equivalent to f(x1, x2, x3) = Σ m(2, 3, 4, 6, 7)

## Slide 66: minterms and Maxterms (with three variables)

## Slide 67
The POS expression is:
This could be simplified as follows:

## Slide 68: Recall Property 14b
14a. x  y + x 
14b. (x + y)(x +
Combining
y = x
y) = x

## Slide 69: POS realization of the function
x1
f
x3
x2
[ Figure 2.29a from the textbook ]
The POS expression is: f = (x1 + x2) (x2 + x3)

## Slide 70: More Examples

## Slide 71: Example 2.14
Implement the function f(x1, x2, x3) = Σ m(2, 3, 4, 6, 7)
using only NAND gates.

## Slide 72: Example 2.14
Implement the function f(x1, x2, x3) = Σ m(2, 3, 4, 6, 7)
using only NAND gates.
The SOP expression is: f = x2 + x1x3

## Slide 73: NAND-gate realization of the function
[ Figure 2.30 from the textbook ]
f
f
(a) SOP implementation
(b) NAND implementation
x2
x3
x1
x3
x1
x2

## Slide 74: Example 2.13
Implement the function f(x1, x2, x3) = Σ m(2, 3, 4, 6, 7)
using only NOR gates.

## Slide 75: Example 2.13
The POS expression is: f = (x1 + x2) (x2 + x3)
Implement the function f(x1, x2, x3) = Σ m(2, 3, 4, 6, 7)
using only NOR gates.

## Slide 76: NOR-gate realization of the function
x1
f
(a) POS implementation
(b) NOR implementation
f
x3
x2
x1
x3
x2
[ Figure 2.29 from the textbook ]

## Slide 77: Implementation with Chips

## Slide 78
Figure B.21. A 7400-series chip.
(a) Dual-inline package
(b) Structure of 7404 chip
V
DD
Gnd

## Slide 79
Figure B.22. An implementation of f = x1x2 + x2x3.
V
DD
x
1
x
2
x
3
f
7404
7408
7432

## Slide 80: Multiplexers

## Slide 81: 2-to-1 Multiplexer (Definition)
Has two inputs: x1 and x2
Also has another input line s
If s=0, then the output is equal to x1
If s=1, then the output is equal to x2

## Slide 82: Graphical Symbol for a 2-to-1 Multiplexer
[ Figure 2.33c from the textbook ]

## Slide 83: Analysis of the 2-to-1 Multiplexer (when the input s=0)
x1
0

## Slide 84: Analysis of the 2-to-1 Multiplexer (when the input s=1)
x2
1

## Slide 85: Analogy: Railroad Switch
http://en.wikipedia.org/wiki/Railroad_switch]

## Slide 86: Analogy: Railroad Switch
http://en.wikipedia.org/wiki/Railroad_switch]
select
x1
x2
f

## Slide 87: Analogy: Railroad Switch
http://en.wikipedia.org/wiki/Railroad_switch]
select
x1
x2
f
This is not a perfect analogy because the trains can go in either direction,
while the multiplexer would only allow them to go from top to bottom.

## Slide 88: Truth Table for a 2-to-1 Multiplexer
[ Figure 2.33a from the textbook ]

## Slide 89: Let’s Derive the SOP form

## Slide 90: Let’s Derive the SOP form

## Slide 91: Let’s Derive the SOP form
s x1 x2
s x1 x2
s x1 x2
s x1 x2
Where should we
put the negation signs?

## Slide 92: Let’s Derive the SOP form
s x1 x2
s x1 x2
s x1 x2
s x1 x2

## Slide 93: Let’s Derive the SOP form
s x1 x2
s x1 x2
s x1 x2
s x1 x2
f (s, x1, x2) =
s x1 x2
s x1 x2
s x1 x2
s x1 x2
+
+
+

## Slide 94: Let’s simplify this expression
f (s, x1, x2) =
s x1 x2
s x1 x2
s x1 x2
s x1 x2
+
+
+

## Slide 95: Let’s simplify this expression
f (s, x1, x2) =
s x1 x2
s x1 x2
s x1 x2
s x1 x2
+
+
+
f (s, x1, x2) =
s x1 (x2 + x2)
s (x1 +x1 )x2
+
+

## Slide 96: Let’s simplify this expression
f (s, x1, x2) =
s x1 x2
s x1 x2
s x1 x2
s x1 x2
+
+
+
f (s, x1, x2) =
s x1 (x2 + x2)
s (x1 +x1 )x2
+
+
f (s, x1, x2) =
s x1
s x2
+

## Slide 97: Circuit for 2-to-1 Multiplexer
f
x
1
x
2
s
f
s
x
1
x
2
0
1
(c) Graphical symbol
(b) Circuit
[ Figure 2.33b-c from the textbook ]
f (s, x1, x2) =
s x1
s x2
+

## Slide 98: Analysis of the 2-to-1 Multiplexer (when the input s=0)
1
0
0
x1
x1
x1
x2
s
f
0

## Slide 99: Analysis of the 2-to-1 Multiplexer (when the input s=1)
1
0
1
x2
0
x2
x1
x2
s
f

## Slide 100: Analysis of the 2-to-1 Multiplexer (when the input s=0)
x1
0

## Slide 101: Analysis of the 2-to-1 Multiplexer (when the input s=1)
x2
1

## Slide 102: More Compact Truth-Table Representation
0
0
0
0
0
0
1
0
0
1
0
1
0
1
1
1
1
0
0
0
1
0
1
1
1
1
0
0
1
1
1
1
(a)
Truth
table
s
x1
x2
f (s, x1, x2)
[ Figure 2.33 from the textbook ]
0
1
f (s, x1, x2)
s
x1
x2

## Slide 103: 4-to-1 Multiplexer

## Slide 104: 4-to-1 Multiplexer (Definition)
Has four inputs: w0 , w1, w2, w3
Also has two select lines: s1 and s0
If s1=0 and s0=0, then the output f is equal to w0
If s1=0 and s0=1, then the output f is equal to w1
If s1=1 and s0=0, then the output f is equal to w2
If s1=1 and s0=1, then the output f is equal to w3

## Slide 105: 4-to-1 Multiplexer (Definition)
Has four inputs: w0 , w1, w2, w3
Also has two select lines: s1 and s0
If s1=0 and s0=0, then the output f is equal to w0
If s1=0 and s0=1, then the output f is equal to w1
If s1=1 and s0=0, then the output f is equal to w2
If s1=1 and s0=1, then the output f is equal to w3
We’ll talk more about this when we get
to chapter 4, but here is a quick preview.

## Slide 106: Graphical Symbol and Truth Table
[ Figure 4.2a-b from the textbook ]

## Slide 107
Analysis of the 4-to-1 Multiplexer
( s1=0 and s0=0 )
w0
0
0

## Slide 108
Analysis of the 4-to-1 Multiplexer
( s1=0 and s0=1 )
w1
1
0

## Slide 109
Analysis of the 4-to-1 Multiplexer
( s1=1 and s0=0 )
w2
0
1

## Slide 110
Analysis of the 4-to-1 Multiplexer
( s1=1 and s0=1 )
w3
1
1

## Slide 111: The long-form truth table

## Slide 112: The long-form truth table
[http://www.absoluteastronomy.com/topics/Multiplexer]

## Slide 113: The long-form truth table
[http://www.absoluteastronomy.com/topics/Multiplexer]

## Slide 114: The long-form truth table
[http://www.absoluteastronomy.com/topics/Multiplexer]

## Slide 115: The long-form truth table
[http://www.absoluteastronomy.com/topics/Multiplexer]

## Slide 116
4-to-1 Multiplexer (SOP circuit)
[ Figure 4.2c from the textbook ]
f = s1 s0 w0 + s1 s0 w1 + s1 s0 w2 + s1 s0 w3

## Slide 117
Analysis of the 4-to-1 Multiplexer
( s1=0 and s0=0 )
0
0

## Slide 118
Analysis of the 4-to-1 Multiplexer
( s1=0 and s0=0 )
0
0
1
1
0
1
1
0
0
0

## Slide 119
Analysis of the 4-to-1 Multiplexer
( s1=0 and s0=0 )
0
0
w0
0
0
0
1
1
0
1
1
0
0
0

## Slide 120
Analysis of the 4-to-1 Multiplexer
( s1=0 and s0=0 )
0
0
w0
0
0
0
w0
1
1
0
1
1
0
0
0

## Slide 121
Analysis of the 4-to-1 Multiplexer
( s1=0 and s0=1 )
0
1
0
w1
0
0
w1
0
1
1
1
0
0
1
0

## Slide 122
Analysis of the 4-to-1 Multiplexer
( s1=1 and s0=0 )
1
0
0
0
w2
0
w2
1
0
0
0
1
1
0
1

## Slide 123
Analysis of the 4-to-1 Multiplexer
( s1=1 and s0=1 )
1
1
0
0
0
w3
w3
0
0
1
0
0
1
1
1

## Slide 124: 4-to-1 Multiplexer (alternative implementation)

## Slide 125
Using three 2-to-1 multiplexers
to build one 4-to-1 multiplexer
[ Figure 4.3 from the textbook ]

## Slide 126
Analysis of the Hierarchical Implementation
( s1=0 and s0=0 )
[ Figure 4.3 from the textbook ]
0
0
0
0
0
w0
w0
w2

## Slide 127
Analysis of the Hierarchical Implementation
( s1=0 and s0=1 )
[ Figure 4.3 from the textbook ]
1
0
0
1
1
w1
w1
w3

## Slide 128
Analysis of the Hierarchical Implementation
( s1=1 and s0=0 )
[ Figure 4.3 from the textbook ]
0
1
1
0
0
w2
w0
w2

## Slide 129
Analysis of the Hierarchical Implementation
( s1=1 and s0=1 )
[ Figure 4.3 from the textbook ]
1
1
1
1
1
w3
w1
w3

## Slide 130: Analogy: Railroad Switches
http://en.wikipedia.org/wiki/Railroad_switch]

## Slide 131: Analogy: Railroad Switches
http://en.wikipedia.org/wiki/Railroad_switch]
s1
w0
f
w1
w2
w3

## Slide 132: Analogy: Railroad Switches
http://en.wikipedia.org/wiki/Railroad_switch]
s1
w0
f
w1
w2
w3
these two
switches are
controlled
together
s0

## Slide 133: 16-to-1 Multiplexer

## Slide 134
w
8
w
11
s
1
w
0
s
0
w
3
w
4
w
7
w
12
w
15
s
3
s
2
f
16-to-1 Multiplexer
[ Figure 4.4 from the textbook ]

## Slide 135
[http://upload.wikimedia.org/wikipedia/commons/2/26/SunsetTracksCrop.JPG]

## Slide 136: Questions?

## Slide 137: THE END